## Slide 1: Crafting Fine Wines in a Challenging Year
Or... What’s your best bet when Mother Nature deals you a challenging hand at harvest?
Presented by Corrie Krehbiel with the support of Cellar-Tek Supplies & WIGA

## Slide 2: Seminar Outline
Strategies to Ensure a Successful Fermentation in Difficult Environments
Techniques to Reduce Green Characters
Processing Grapes with Botrytis and Rot
Methods for Enhancing Mouthfeel and Achieving Wine Balance

## Slide 3: Successful Fermentation Strategies
In the Vineyard
  Fruit Maturity
    pH, TA, Brix
    Flavour Development
    Phenolic Ripeness
    Disease Pressures
    Sampling Procedure
At Harvest
  Trained crews
  Rapid Pick to Processing Times

## Slide 4: Successful Fermentation Strategies
Processing Considerations
  Sorting
  Crushed or Whole Cluster?
    Crushed Fruit:
      Advantages:
        Less press space required
        Increased yield
      Disadvantages:
        Increased solid content
        Increased harsh phenolics

## Slide 5: Processing Considerations
    Whole Cluster
      Advantages:
        Fewer Solids
        Less Sensitive to Oxidation
        Fewer Harsh Phenolics
      Disadvantages:
        Smaller press loads,
        i.e. “Takes more time”
  Maceration Time

## Slide 6: Pre-fermentation Analysis
Why do I need to analyze my juice?
Components to analyze:
    pH, TA, Brix, YAN
Why Measure YAN?
    To determine the amount of nitrogen that is needed to ensure a successful fermentation.
    Note: if the YAN is <140 mg/L, it will also be lacking in lipids; therefore, yeast enhancers (Dynastart/Fermoplus Energy Glu) are necessary.

## Slide 7: How to Measure Assimilable Nitrogen
Take 50mL of Clarified Must
Adjust the solution to pH 8.5 with 1N NaOH
Add 20mL Formaldehyde
Wait 2-3 Minutes.
Titrate with 0.1N NaOH until the pH is back to 8.5 (The number of ml needed is “n”)
YAN (mg/L) = n x 28

## Slide 8: Juice Additions And Adjustments
SO2
    Used to protect the juice from oxidation
    Prevents the multiplication of spoilage organisms
Enzymes
    In the grape and juice stage, pectolytic enzymes are used
    Functions:
      Increases free run yield
      Improves settling
    Temperature is Important!!
    Consider your variety
    Note: Pectolytic enzymes with B-glucosidase activities may be used later. Glucanases may be used later with grapes with rot.

## Slide 9: Juice Additions and Adjustments
De-acidification
    Potassium Carbonate or Potassium Bicarbonate
      PPT of Potassium Bitartrate
      Decrease of 1g/L requires
        0.9g/L Potassium Bicarbonate
        0.62g/L Potassium Carbonate
      Potassium bicarbonate easily precipitates by chilling
      Example: Deacid
    Calcium Carbonate
      PPT of Calcium Tartrate
      Decrease of 1g/L requires 0.45 g/L Calcium Carbonate
      Chilling has little effect on ppt of calcium tartrate

## Slide 10: Juice Additions and Adjustments
    Double Salt
      Acidex
      A preparation of calcium carbonate which also contains double salt crystals
      Method
        Only a portion is de-acidified
        The Calcium carbonate present raises the pH above 4.5
        pH is essential to dissociate the tartaric and malic forms sufficiently
        At pH > 4.5 the malate and tartrate combine rapidly to form the double salt
Got Sour wine?

## Slide 11: Juice Additions and Adjustments
Chapitalization
    The addition of sugar with the intent to raise the concentration of alcohol
    Conversion Ratio:
      To increase alcohol 1%, 17 g/L of sugar is required
      In reds, often 20 g/L is required
    Ensure that the sugar is dissolved
    Ensure that the sugar is added at the beginning of fermentation when the wine is not depleted of nutrients

## Slide 12: Juice Additions and Adjustments
Juice Fining
  Why Juice Fine?
    Reduction of bentonite need later
    Removal of “pinking”
    Oxidative protection
    Aromatic precursor protection
    Retention of fresh, fruit characters
    Reduction of rot odours
    Clarification
  Risks
    Over-fining
    Juice that is too clear
  Juice fining agents
    Bentonites, Gelatins, Mixed agent blends
Notes: Insert South African Juice fining Picture

## Slide 13: Steps to Achieving a Successful Fermentation
Selection of the Yeast Strain
    Know your factors:
      Grape Condition and Analysis
      Your goal (stylistic objective)
      Cellar restraints
    (Tasting Of Pinot Gris Yeasts)
Timing of Inoculation
    Inoculate as soon as possible to avoid multiplication of indigenous flora and nutrient reduction.

## Slide 14: Steps to a Successful Fermentation
Rehydration Method
    Use a Clean Container
    Add Chlorine Free Water at 37°C to the Container (10x the weight of the yeast)
    Add a Yeast Rehydration Nutrient (Dynastart, Fermoplus Energy Glu) Why?
          Improved Aromatics
          Improved Temperature Tolerance
          Improved Alcohol Tolerance
          Improved Cell Viability at the End of Fermentation

## Slide 15: Steps to A Successful Fermentation
  Add 20-25 g/hL of yeast
  Let sit for 20 minutes
  CHECK THE TEMPERATURE DIFFERENCE BEFORE ADDITION – MUST NOT BE GREATER THAN 10 C
  Other Keys:
  Temperature at beginning and end of AF
  Aeration and turbidity

## Slide 16: Treating Under Ripe Grapes
Considerations when Treating Unripe Grapes
    Limited Extractability
    Unripe Grape and Seed Tannins
    Green Characters
Limited Extractability
    Due to thicker skins
    Enzyme Use: Lafase Fruit, Contact Pelliculaire, Endozym Cultivar
    Protect your skin tannins!!

## Slide 17: Treating Unripe Grapes
Addressing Unripe Seed Tannins
  De-seed
  Limit Maceration time (especially extended)
  Ensure colour stabilization
Dealing with Green Character
  Yeast Choice (Pinot Noir Tasting)
  Untoasted Oak in Fermentation
  Aging Tannins and Mannoproteins

## Slide 18: Treating Grapes with Rot and Botrytis
Botrytis Cinerea
  Mycelium fungus – aka grey mould
  Develops on the grapes and forms small grey-white filaments
Why is Botrytis a problem?
  Laccase production
          LACCASES = OXIDATION + BROWNING
  Glucanases
          GLUCANASES = PLUGGED FILTERS
  Mouldy/Compost aromas
  Fermentation issues due to toxins produced by botrytis

## Slide 19: Treating Grapes with Rot and Botrytis
How to combat rot and botrytis
  Add Tannins Early
    Protects colour
    Inhibits laccases
    Provides oxidative protection
    Improves structure of the finished wine
  Use Enzymes
    β- 1,3 and 1,6 glucanases degrade the glucans (and improve filterability)
    Add Mid-way through fermentation
    Examples: Extralyse, Endozym Antibotrytis

## Slide 20: Treating Grapes with Rot and Botrytis
Reduce or Eliminate Maceration Time!
Choose Yeast Wisely!
      Short Lag Phase
      Strong Fermentation Kinetics
OXIDATION

## Slide 21: Treating Grapes with Rot and Botrytis
Handle Gently
    Pre-fermentation
    During Fermentation
    Examples.......

## Slide 22: Botrysized White Wine Production
Sort Grapes
    In the field
    Pre-processing
De-stem and Crush Gently (or whole cluster).
    Add Pectinase (Endozym ICS 10 Eclair, Endozym Cultivar, Lafazym CL)
Add Gallic Tannin
      5 g/hL (up to 10 – 12 g/hL depending on grape quality)
      Galalcool, Gallovin

## Slide 23: Botrysized White Wine Production
Fine the juice
      Examples:
      Polylact (PVPP-casein) and bentonite
      Argilact (Casein and bentonite)
      Microcel (Casein and bentonite)
      Biocatalasi
Inoculate
      With Strong Culture / Short Lag Phase
          X5, X16, Fermol Arome Plus
      Use rehydration nutrients and ensure adequate juice nutrition

## Slide 24: Botrysized White Wine Production
Ferment and Rack Anaerobically
  Until laccases are destroyed
  Add SO2 and rack early
Use glucanase mid-late fermentation
  Endozym Antibotrytis, Extralyse

## Slide 25: Botrysized Red Wine Production
Sort Grapes
    In the field
    Pre-processing
Destem and Crush Gently
    Add 70-80 ppm of SO2 at the crusher
    Add VR Supra or Fermotan as tank is being filled (30-70 g/hL).
    Add 3-5 g/hL of Gallovin or Galalcool if rot pressure is extreme
    Add enzyme for gentle extraction – Lafase fruit, Contact Pelliculaire

## Slide 26: Botrysized Red Wine Production
Limit or Avoid Maceration
Inoculate
      With Strong Culture / Short Lag Phase
          FX10, Fermol Mediteranne
      Use rehydration nutrients and ensure adequate juice nutrition
Consider VR Colour for Colour Stabilization
Limit Pumpovers/Punchdowns
Mid-ferment add B-glucanase
Press early

## Slide 27: Enhancing Mouth Feel After Fermentation
Mannoproteins
    Yeast Cell Wall
    Mimic lees aging
    Rounds out mid-palate and masks bitterness
    Biolees MP, Battonage Elevage, Battonage Plus Structure

## Slide 28: Enhancing Mouth Feel After Fermentation
Gum Arabic
    Large polysaccharide gum
    Introduced initially for tartrate stability
    Viscous – gives perception of sweetness
    Add Last!!
    Stabivin, Arabinol

## Slide 29: Enhancing Mouth Feel After Fermentation
Aging Tannins
  Proanthocyanidinic (seeds & skins)
    Build structure and fill in gaps
  Ellagic (seasoned oak tannins)
    Improve Structure and Aromatics

## Slide 30: Thank-you.
I appreciate your time to attend this seminar and sincerely hope you were able to take away some useful information to help you make the best wines you can, even in a challenging harvest like the one that looks like it’s shaping up out there as we speak...
If you’d like to discuss anything from any of the slides further, don’t hesitate to contact me directly.
Corrie Krehbiel ckrehbiel@cellartek.com
250-878-5957